## Slide 1
Sensors
Microphone sensor
SKU:SEN0487
Távolság szenzor
BME280
Gyroscope sensor
Adafruit 9-DOF Orientation IMU Fusion Breakout - BNO08
Távolság szenzor
HCSR – 04
USER Interfaces
Push Button 1
SKU: DFR:0029
Activate the drill
Digital Buzzer
Digital Buzzler V2
RGB LED 1
(Active/Inactive indicator)
RGB LED 2
(Drill was stopped)
Adaptive drive
Drón szervó
MM0120K-POWER
Precision servo
MM0120K-POWER
Drón szervó
Grove - I2C Motor Driver with L298
Motor Driver
Grove - I2C Motor Driver with L298
SPI0/I2C0
SPI1/ I2C1
Pushrod, transmission
Original Push Button(Start drive, given RPM control)
Central controller
ESP32 DevKit Board(36 pin version)
External connectionBuilt-in Bluetooth module
Power Side
5V
7,4 V
DC-DC Converter
DCDC3VU 3A adjustable step down power supply module with voltmeter
Li-Po battery
18650 battery pack
7,4 V
7,4 V
A
A
Push Button 2
SKU: DFR:0029
Slave the Orientation
Digital I/O
Digital I/O
PWM1
Push button 3
(Mechanical emergency stop)
3 x ADC (R, G, B)
3 x ADC (R, G, B)
UART1/SPI/I2C
ADC 4
2xPWM
Gyroscope sensor and accelerometer
Grove - 3-Axis Digital Accelerometer
SPI/I2C/GPIO ADC
Magnetic Encoder
3.8 - 24 V, Hamlin 55100-3H-02-A
(Magnet and Capacitor Recuired)
A5
Output type "Sink" 3-wire
Used peripherias of the microcontroller:
  4 ADC
  4 DI/O
  1 I2C
  1 UART
  3 SPI
  7 PWM
Legend:
Digitális jel
PWM jel
UART
ADC/DAC
SPI
I2C
Drón szervó
MM0120K-POWER
Limit switches
V156 1C25
2 x Digital I/O
LikeABosch: Hardver Challenge
I2C1
5V feed line
7,4V feed line
Driveing Dept Control
Drón szervó
MM0120K-POWER
Precision servo
Stepper motor No 17 with 300mm screw
Drón szervó
Grove - I2C Motor Driver with L298
Motor Driver
DRV8825 Stepper Motor Driver Carrier
Pushrod, transmission
Mechanical interface
7,4 V
7,4 V
4*A
4*A
2xPWM
2xPWM